Determining the Phosphate Content in Fertilizers

Introduction:

Fertilizers are widely used to improve the growth of crops.  Many of these fertilizers contain phosphates..  This experiment will determine the amount of phorous

present as phosphate.

Purpose:

The purpose of this experiment is to determine the amount of phosphorous present in a soluble fertilizer in the form of the phosphate ion.

Equipment/ Materials

HACH kit and supplies for the Phosphorus, Reactive (Orthophosphate) test (number 490)

10 mL sample cells

PhosVer3 phosphate Powder Pillow

Standard phosphate solution Na3PO4.12H2O 50.0 mg/L

Volumetric flasks (25 mL)

Pipet (10 mL)

Pipet bulb

Kim wipes

Automatic pipet adjustable

Solutions of fertilizers containing phosphate

Safety:

Wear an apron and goggles

Procedure:

- Use the 50 mg/L Standard solution to prepare 25 mL of standards containing 2.4 mg/L, 1.0 mg/L, 0.75 mg/L and 0.5 mg/L of phosphate.  Also prepare a blank.  The blank in this case is a 10 mL sample cell of distilled water.

- Measure the concentration of each of these standards using the DR 2400 from the HACH kit.

  - Touch favorite programs

  - Select program 490 P React. PV

  - Touch Start

  - Fill a round 10 mL sample cell with 10 mL of a standard

  - Add the contents of one PhosVer 3 phosphate Powder Pillow to the standard.  Immediately cap and invert to mix.  This becomes the prepared sample

  - Touch the clock in the lower left side of the screen.  This is the timer icon.

  - Touch Start.  The clock begins to count down as a two-minute reaction period is started. Place the prepared sample vial on the lab table.

  - Wipe the blank and place it into the cell holder.

  - When the timer beeps, Touch Zero.  The display will show 0.0 mg/L PO43-.

  - Within one minute after the timer beeps, (indicating completion of the Zero reading), wipe the prepared sample and place it into the cell holder.

  - Touch Read.

  - Results will appear in mg/L PO43-.  Record data

  - Repeat until all standards have been measured.  Record data.

- Obtain a sample of fertilizer solution

- Repeat step 2 using the fertilizer solution.  Record data

- Repeat step 2 using additional fertilizers.  Record data

Data:

Standards

| Prepared Concentration (mg/L) | HACH meter reading (mg/L) |
| --- | --- |
| 2.4 |  |
| 1.0 |  |
| 0.75 |  |
| 0.5 |  |

Fertilizer

Kind of fertilizer used ______________________________________

HACH meter reading _______________________________________

Kind of fertilizer used ______________________________________

HACH meter reading _______________________________________

Kind of fertilizer used ______________________________________

HACH meter reading _______________________________________

Calculations:

- Using the equation C1V1 = C2V2, calculate the volume of 50.0 mg/L PO43- solution needed to prepare 25 mL of a solution containing 2.4 mg/L PO43-

- Using the equation C1V1 = C2V2, calculate the volume of 50.0 mg/L PO43- solution needed to prepare 25 mL of a solution containing 1.0mg/L PO43-

- Using the equation C1V1 = C2V2, calculate the volume of 50.0 mg/L N solution needed to prepare 25 mL of a solution containing 0.75 mg/L PO43-

- Using the equation C1V1 = C2V2, calculate the volume of 50.0 mg/L PO43- solution needed to prepare 25 mL of a solution containing 0.50 mg/L PO43-

- Graph your data.  Plot the prepared concentrations on the x axis and the HACH meter readings on the Y axis

- Using the calibration curve constructed above and the HACH meter reading, calculate the concentration of PO43- in your fertilizer.

Questions

- Why was a calibration curve constructed.?

- List three errors that would cause phosphate readings to be too low.

- List two errors that would cause phosphate readings to be too high.